## Slide 1
523491 COOPERATIVE EDUCATION I
นางสาวปอรรัชม์ ปานใจนาม
รหัสนักศึกษา B6109868

## Slide 2
Sony
Technology (Thailand)
Co., Ltd.
STTB

## Slide 3
Position:
COOP STUDENT
• ลักษณะงานที่ได้รับมอบหมาย คือ งานประจำและโครงงาน
• งานที่ได้รับมอบหมาย คือ Implement Intelligent Manufacturing with IoT,
One STT project (การพัฒนาเว็บไซต์และโปรแกรมเพื่อระบบโรงงาน), เขียน Web Application ด้วย C#, JAVA Script, PHP, SQL, HTML อื่น ๆ ตามที่ได้รับมอบหมาย โดยปฏิบัติงานที่โรงงานบางกะดี จ.ปทุมธานี
Department:
New Technology & System development

## Slide 4
เพื่อเรียนรู้ในการพัฒนาเว็บไซต์และโปรแกรมเพื่อระบบโรงงาน
เพื่อนำความรู้ไปใช้ให้เกิดประโยชน์ในอนาคตได้
เพื่อเรียนรู้และเข้าในการทำงานจริงภายในสถานประกอบการ
วัตถุประสงค์

## Slide 5
ศึกษาการทำงานของระบบโรงงาน
ศึกษาการใช้งานซอฟแวร์ที่เกี่ยวข้องกับการพัฒนาเว็บไซต์และโปรแกรมเพื่อระบบโรงงาน
ศึกษาการใช้งาน PHP HTML JavaScript และ MySQL
ขอบเขตการทำงาน

## Slide 6
ในปัจจุบันการทำงานอย่างมีประสิทธิภาพถือเป็นเรื่องสำคัญ กล่าวคือพนักงานที่ทำงานนั้นควรมีสุขภาพร่างกายแข็งแรงพร้อมสำหรับการทำงาน แล้วเป็นหน้าที่ของทางบริษัทที่ต้องใส่ใจดูแลพนักงานทุกคนโดยมีการตรวจสอบดูแลสุขภาพและความเสี่ยงต่าง ๆ ของพนักงานที่อาจเกิดจากการทำงานได้ เนื่องจากพนักงานมีจำนวนมากและวิธีการเดิมที่ใช้ตรวจสอบดูแลพนักงาน เพื่อทำการแจ้งให้ไปตรวจสุขภาพตามรายการความเสี่ยงในการทำงานส่วนนี้ใช้เวลาในการทำงานเป็นเวลามากจากปัญหาข้างต้น
จึงทำให้เกิดแนวคิดในการจัดการปัญหานี้ภายในองค์กรเพื่อให้ลดเวลาการทำงานในส่วนนี้ของผู้ตรวจสอบดูแลพนักงาน และอำนวยความสะดวกในการตรวจสอบมากยิ่งขึ้นจึงเกิดการจัดทำระบบแจ้งตรวจสุขภาพตามปัจจัยเสี่ยงของพนักงานขึ้นมา
ที่มาและความสำคัญ

## Slide 8
Health Checkup risk factor system
ระบบแจ้งตรวจสุขภาพตามปัจจัยเสี่ยงของพนักงาน
Tools

## Slide 18
ผลการปฏิบัติงาน
1. การปฏิบัติงานด้านสังคม
- ได้ฝึกการเรียนรู้ในการสื่อสารกับผู้อื่นในการทำงานเป็นทีม และการทำงานร่วมกันกับผู้อื่น
- ได้เรียนรู้วัฒนธรรมภายในองค์กร
- ได้รู้จักการแบ่งเวลา การวางแผนและมีความรับผิดชอบต่องานที่ได้รับมอบหมาย
- ได้ฝึกทักษะการปรับตัวและการแก้ปัญหาต่าง ๆ
2. การปฏิบัติงานด้านทฤษฎี
- ได้เรียนรู้การเขียน PHP, HTML, JavaScript และ MySQL
3. การปฏิบัติงานด้านการปฏิบัติ
- ได้ฝึกทักษะในการสื่อสารกับผู้อื่นในการทำงาน เพื่อให้งานที่ได้รับมอบหมายเป็นไปอย่างราบรื่น
- ได้นำความรู้ที่เรียนมาประยุกต์ใช้ในการเพิ่มทักษะในอนาคต
- ได้เรียนรู้การแก้ปัญหา

## Slide 19
สรุปผล และข้อเสนอแนะ
จากการที่ได้มาปฏิบัติงานสหกิจศึกษาที่แผนก New technology and System development ของ บริษัท โซนี่เทคโนโลยี (ประเทศไทย) จำกัด เป็นระยะเวลา 16 สัปดาห์นั้น นอกจากจะได้นำความรู้ที่ได้เรียนมาประยุกต์ใช้โดยการปฏิบัติงานจริงแล้วยังได้รับความรู้ใหม่ ๆ เพิ่มเติมอีกมากมาย ซึ่งเป็นประสบการณ์ที่ดีที่จะนำไปปรับใช้ในการทำงานจริงในอนาคตต่อไป

## Slide 20
สรุปผล และข้อเสนอแนะ
1. ปัญหาและอุปสรรคที่ส่งกระทบต่อการดำเนินงาน
- ปัญหาในการปรับตัวในการทำงาน เนื่องจากเป็นการมาสหกิจศึกษาครั้งแรก
- ปัญหาด้านการเรียนรู้งาน เนื่องจากในช่วงแรกได้รับมอบหมายงานในเนื้อหาที่ไม่เคยได้ศึกษามาก่อน ซึ่งทำให้ไม่ คุ้นเคยกับภาษาที่ใช้
- ปัญหาด้านสุขภาพ เนื่องกระทบจากการแผ่ระบาดของ COVID - 19

## Slide 21
สรุปผล และข้อเสนอแนะ
2. ข้อเสนอแนะ
- นักศึกษาควรมีความกล้าแสดงออกในการสื่อสาร และสอบถามความต้องการหรือหากมีข้อสงสัยควรปรึกษาพนักงาน ที่ปรึกษาทันที เพื่อให้งานที่ได้รับมอบหมายออกมาดีและรวดเร็ว
- นักศึกษาควรศึกษาหาความรู้เพิ่มเติมอย่างสม่ำเสมอ เพื่อให้สามารถทำงานได้อย่างรวดเร็วและมีประสิทธิภาพมากยิ่งขึ้น
- นักศึกษาควรวางแผนการทำงาน เพื่อให้งานเสร็จตามเวลาที่กำหนดไว้
- นักศึกษาควรวางแผนในการทำงานให้รอบคอบ

## Slide 22
BACC
STTB-AUTO COSMETIC CHECK
STTB SMART TEAM

## Slide 23
Image & Lighting
+
Machine Learning
Cosmetic Check/BACC
Parallel Work
Image
folder
Classification
Image
Machine Learning
Application Flow
Output
Project Charter
Concept: Utilize image processing & lighting technique with new development of machine learning

## Slide 24
Project Charter
Concept: Utilize image processing & lighting technique with new development of machine learning

## Slide 25
STTB-Auto Cosmetic Check
Concept | Purpose of Project
BACC is automatic detection smartphone defect robot. Implement machine learning + AI for classify OK/NG | 1. Reduce HC and decreasing human error in this process and increasing the accuracy of detection. 2.This project will build the standard detection for inspection process. 3.Developing new technology in production for improve efficiency and productivity.
** This project we use some equipment from APC machine (PJ in FY17)
But develop the software by STT member

## Slide 26
STTB-Auto Cosmetic Check
Item | Detail | Inspector OPT | APC | BACC
Investment | Additional cost | N/A | N/A | 40K THB (new Light source)
Manpower | Total operator | 1 | 2 (Take a Photo 1 HC, Judgement 1 HC) | 1 (Manual Case) 0 (Automatic)
Operation | Load In-Out | N/A | Manual | Manual (Can use DOBOT for Automatic)
 | Scanning | Manual | Manual | Manual / Automatic
 | Inspection Judgment |  | Manual | Manual / Automatic
 | Operation Time / MC | 23 sec | 53.69 Sec. | ~ 60 Sec. (Plan to reduce to 40 sec)
Quality | Can detect defect and descript the position of defect | Can | Can | Can
Automation | Can implement robotic | Can’t | Can | Can
Software development | Machine control | N/A | Dev by SGMO | Use STT S/W
 | Lighting control | N/A | Use SGMO S/W | Use STT S/W
 | Image processing | N/A | Use SGMO S/W | Use NI Vision
 | AI processing | N/A | Upload to Cloud server | Use local PC
 | License cost | N/A | Yearly payment to SGMO | 0
Summary # Performance  Able to judge OK/NG by machine. # Investment  Cost estimation for additional part.  40K THB per machine
 We can utilize the old part from APC machine
Comparison between OPT vs APC vs BACC
#Benefit  Reduce Inspector HC.  Can implement for Full Automation Line. #ROI  ### TBD ###

## Slide 27
#Time Plan for BACC [Trial in PDX223 PVT+SS2]

## Slide 28
SMART Room
STTB Production Line Area
STTB Engineer
43.72.228.147
THSTTBMESSUB04 (Smart Portal)
To monitor BACC data
AP SEN
SEC @Sony
STTB RAS
Internet
Internet
RAS
RAS
BACC System Infrastructure
AI Training System
BACC Machine#1
SOMC RAS
VLAN10 122.123.x.x
Production Network
Firewall
STTB Production
BACC Machine#2
Firewall
STTB MES Server
VLAN10 122.123.x.x
Production Network
Not design to access BACC yet
To prevent IP photo leak
Upload photo to SMART system with permission
Access the machine remote from SMART Office
This machine use for train AI
And develop image processing
This machine use for input actual phone
1
2
3
4
5
6
7

## Slide 29
Option#1  Place it after CUWRT
Clean
Insert Jacket
Remove Jacket
Pros:
It can detect defects before input to the CT line. To guarantee the phone has no defect before CT.
The photo from this M/C can use to compare after CT.
It can connect the line to full automation
It can reduce 1 HC (INSPCU-Assy)
Cons:
Need to add the processes to remove the jacket and insert the jacket
It can not detect defects that appear after CT line

## Slide 30
Option#2  Place it after CU INSP
Pros:
It can detect overall defects from CU to CT line.
It can connect the line to full automation
It can replace the current logo check machine
It no need to insert a Jacket after the cosmetic check
The photo from this M/C can use to compare with SI inspection.
Cons:
It can not detect defects that occur before CT.
  It’s too late detection
It can not reduce H/C
Clean
Remove Jacket
By OPT
Current

## Slide 31
Option#3  Place it after SI Laser marking
Pros:
It can guarantee the pho before shipping to the customer
It can connect the SI line to be full automation
It can replace the current logo check machine
It does not concern a Jacket
The photo from this M/C can use to verify when market claims
Cons:
It can not detect defects that occur in the CU process. It’s too late detection
It can not reduce H/C (Just replace Logo check M/C)

## Slide 32
BACCPDX223 SS2 + BACC Trial
STTB SMART TEAM

## Slide 33
AI Inspection
We use 2 models in process ,REAR and SIDE, that trained by DNN+ResNet50 which is perform well in image classification.
AI Model
Inspection data will update in realtime to
BACC Station report web
(http://43.72.228.147/wbacc/lastest_training.php)
Realtime Data Update
AI Inspection is running with PENGUIN and NI Vision at the same time
Parallel Work

## Slide 34
AI Model
After receive image from NI Vision ,We cut image and ready to image classifying process. Model Image clasiifying by Resnet50 is a convolutional neural network that is 50 layers deep after check image with all OK and NG trait, AI will sort all accuracy from each class and select most accuracy to be output (more than 50%)
Example Output
AI predict OK
and actually OK
AI predict NG and actually NG

## Slide 35
Input training image
We cut image into small part to see more detail
Position | Parts
Rear Top | 20
Rear Center | 20
Rear Bottom | 20
Side Top | 5
Side Left | 5
Side Right | 5
Side Bottom | 5
Rear | Side
2,471 files | 4,236 files
* With small images AI can see more detail and regconize defect better than use large scale image.
But with more image, it make analysis process longer than use large image.
Bottom
Top
Left
Right
Rear

## Slide 36
ML Model of PDX223
We used two models, for rear and side ,we train them separately and this is the result of the model.
REAR MODEL
SIDE MODEL
IMAGE: Model 14.02.2022

## Slide 37
Trial Summary
Color | Set | OK | NG
Black | 14 | 4 | 10
Violet | 7 | 1 | 6
White | 9 | 4 | 5
Frosted Black | 3 | 0 | 3
Frosted Silver | 2 | 0 | 2
Green | 1 | 1 | 0
Leak
8.3%
Correct Inspection
72.22%
Over Reject
19.44%
Result of AI Inspection
Total | 36 | 10 | 26
Correct Inspection : AI can detect defect as same as OPT 26 case
Leak : AI can not find defect 3 case
Over reject : AI predict NG but product actually OK 7 case
*Data from 2021-08-13 to 2022-02-14
*to reduce false predict we have to train AI model with more variety NG and OK trait image.

## Slide 38
Finding issue
Over Reject discolor and dust
Leak dent and dirty

## Slide 39
EXAMPLE OF OVER REJECT
DISCOLOR DEFECT
AI RECONIZE SMALL DISCOLOR POINT AS DEFECT EVEN IT IS ACCEPTABLE
AI RESULT : NG 88% | OK 12%
*Solution : train this image into OK class
AI RECONIZE SMALL DUST AS DEFECT
AI RESULT : NG 58% | OK 42%
*Solution : clean product again before inspect
DUST

## Slide 40
EXAMPLE OF LEAK CASE
DENT DEFECT
Due to camera angle we can't see the dent on button in side part.
AI RESULT : OK 58% | NG 42%
*Solution : Set light to reflect dent
DIRTY DEFECT
AI can't regconize this defect .
AI RESULT : OK 96% | NG 4%
*Solution : train this image into NG class

## Slide 41
BACC Station report website
Home page : show realtime Inspection result from BACC Station the lastest will show detail and analyze all predict result and actual inspection.
image modal to see detail in image.
this page will show only 1 image that have same result as OPT

## Slide 42
Inspection History page : Show table of all inspection history with each row can show more detail and ai result of all image.
we can search to see inspection history in specific period or specific model .
same as home page every image have modal so we can see more detail

## Slide 43
AI Performance page : calculate all inspection history result in database to maesure AI Performance ( using confusion matrix) and show data in 2 chart pattern
First chart show summary of result in 4 catagories (True OK, True NG, Leak, Over reject)
Second chart show summary of result in each day

## Slide 44
Measure AI Performance
Confution Matrix
True OK
True NG
Over reject
Leak
3
2
7
24
Accuracy is calculated as the number of all correct predictions divided by the total number of the dataset
Accuracy = (True OK + True NG)/(True NG + True OK + Leak + Over reject)
Precision is calculated correct predict and actual result of NG or OK class
Precision = (True NG )/(True NG + Leak ) or (True OK )/(True OK + Over reject )
Recall is calculated correct predict and all predict of NG or OK class
Recall = (True NG)/(True NG + Over reject) or (True OK )/(True OK + Leak )
F1-Score is the harmonic mean of precision and recall and is a better measure than accuracy.
F1-Score = 2x(Precision x Recall)/(Precision + Recall)

## Slide 45
Heat map page : show NG heat map of lastest model in inspection history each coordinate can show example image and detail
* Heat map is easy to check If we have a lot NG in same coordinate.So we can analyze the cause of defect and fix before it be more NG.

## Slide 46
Summary
Use DNN+Restnet50 for training model
The Rear model has Accuracy 97.88% and the Side model has Accuracy 98.65%.
Total trial inspection 36 set
BACC station has an inspection accuracy 72.22% (as of 18th Feb)
Rear Model
Side Model

## Slide 47
All Program for INnspection
AI _Trianing.exe - image classify และ เก็บรูปเพื่อนำไป train ต่อ
NI Vision - ถ่ายรูป+image processing
PENGUIN - สำหรับการติดต่อระหว่าง software และ hardware
VSPE หรือ Terminal - สำหรับเชื่อมต่อ COMPORT

## Slide 48
Thank You

## Slide 49
BACC MANUAL FOR USER
1. Open VPSE Add comport and Click Run
2. Open PDX223.vbai and Click Run

## Slide 50
BACC MANUAL FOR USER
3. Open AI Training.exe, Setting and Click Run

## Slide 51
BACC MANUAL FOR USER
4. Open PENGUIN > Load Master Config > Choose model and station( cddr ) > Click Load this config and Click Run

## Slide 52
BACC MANUAL FOR USER
5. Scan MSN and put product on holder when PENGUIN and NI finish capturing picture wait for AI_Training to processed
6. When AI_Training finish loading image we have to check if the result that AI predict is correct and if the result is fault predict we have to click on the image and click the actual result after checking all the result Click done an confirm to finish the process

## Slide 53
All Program for Develop
GX Work - สำหรับเขียน PLC รับค่าจาก PENGUIN รับมาเป็น ASCII(HEX)
PC Interface SW - สำหรับการเขียนตำแหน่งของ Product
ATC Controller - สำหรับการเขียนตำแหน่งของ Ring Light
NI Vision - สำหรับเขียน process ของการ set img processing & snap
Visual Stuio 2019 - พัฒนาModel ของ AI

## Slide 54
AI MODEL
STTB SMART TEAM

## Slide 55
IMAGE INPUT
Path: \\43.72.228.131\cddr\All_Images\ImagesForTrainModel
LASTEST IMAGE INPUT FOR TRAIN MODEL: Model18.02.2022
\\43.72.228.131\cddr\All_Images\ImagesForTrainModel\IMG02.2022\Model18.02.2022
Bottom
Top
Left
Right
Rear
IMAGE INPUT
REAR
NG
OK
SIDE
NG
OK
AIModelRear.zip
AIModelSide.zip
CLASS
TRAIN
MODEL OUTPUT

## Slide 56
STEP TRAIN MODEL
MANUAL: \\43.72.228.131\cddr\คู่มือ
Document
คู่มือ ML.NET Model Builder for Image Classification (Visual Studio 2019)
คู่มือ Test Model
Video
TRAIN_AI_MODEL
path for folder in vdo: \\43.72.228.131\cddr\TRAIN_MODEL